## Slide 1
www.studymafia.org
Submitted To: Submitted By:
www.studymafia.org www.studymafia.org
Seminar
On
Universal Serial Bus

## Slide 2: Content
History and Evolution
Why We Need USB？
Architectural Overview
USB communication flow
Protocol Layer
Conclusion
References

## Slide 3: Key Word
Down：From host to device
Up：From device to host
Example
Down stream：data flow from host to device
Up stream： data flow from device to host

## Slide 4: History
USB—Universal Serial Bus
Invented and standardized by a group of computer and peripherals manufactures in 1995
Compete with IEEE1394

## Slide 5: Evolution

## Slide 6: Why We Need USB？
Connection of the PC to the telephone：
=>In order to transmit data
Ease-of-use：
=>Saupport plug and play
Port expansion：
=>Up to 127 devices
=>Can add lots of device to a XX

## Slide 7: Characteristic (2)
The logical topology of the USB is a star structure
It is similar to computer network
The USB uses a polling protocol
Up to 7 level

## Slide 8: USB Can Do
Combines low speed and high speed bus activity , USB enables shared access for both speed
Automatic configuring of devices and a serial bus which is simplified and easy to plug into
Attach / detach easily without restarting system

## Slide 9: Architectural Overview
Host：only one
=>The smartest element in the USB system
=>Responsible to the complexity of the
protocol to make devices design simple
and low cost
=>Control the media access（no one can
access the bus unless it get an approval required from the host )

## Slide 10: USB System Member (2)
Hub：one or more
=>Like the hubs used for computer network
=>Enables many devices to connect to a single USB port

## Slide 11: USB System Member (3)
Device：one or more
=>Everything in the USB system , which is
not a host , is a device ( include hubs)
=>A device may provides one or more USB
functions
=>Has an unique address at the end of the
enumeration process

## Slide 12: Typical Application

## Slide 13: Communication Flow

## Slide 14: Pipes (1)
The logic communication between the client
software on the host and the function on the
device is done through pipes
It is a association between a specific
endpoint on the device and the appropriate
software in the host

## Slide 15: Pipes (2)
An endpoint is the source or destination of the data that transmitted on the USB cable
Two direction
=>OUT：
data flows from the host to the device
=>IN：
data flows from the device to the host

## Slide 16: Signaling On The Bus
The USB cable is 4 wire cable
Signal on the bus is done by signaling over tow wires ( D+ and D_ )
=>1： D_ low , D+ high
=>0： D_ high , D+ low
Data encoding and decoding is done using NRZI ( Non Return to Zero Inverted )

## Slide 17: SIE
SIE：Serial Interface Engine
It is part of both the host’s and the device’s physical layer
=>Serialization and Deserialization
=>Encoding and Decoding
=>Generate(for out) and Verify(for in) CRC
=>Detect PID

## Slide 18: HC
HC：Host Controller
=>It is an additional hardware to ensure that everything which is transmitted on the bus is correct
=>It serves both the USB and the host and has the same functionality in ever USB system

## Slide 19: This Layer Handles
Responsible for the translating the data between the application layer and the USB transactions protocol .
Two Role
=>USB System Software (in the USB host)
=>USB Logical Device (in the USB device)

## Slide 20: The USB System SW
Compose of The Host Controller Driver and The USB Driver
Responsible for
=>Bandwidth allocation
=>bus power management
Two of above are in order to enable devices to access the bus

## Slide 21: The USB Logical Device
Compose of a collection of independent endpoints
Each endpoint has an unique Endpoint Number and is unidirectional(except endpoint zero and has two type--In/Out)
Default pipe is associated with endpoint zero

## Slide 22: The Application Layer
Host end：Client Software
= >Manages the appropriate interface by
transferring data from its buffers to the
endpoint with the appropriate interface
Device end：Function
= >Composed of interfaces and controls the
functionality of the device

## Slide 23: Protocol Layer
USB transactions are done through packets include three phases
=>Token phase：host initiates token
indicating the future transfer type
=>Data phase：actual data transmitted
=>Handshake phase：indicate the success or failure of the transaction

## Slide 24: Transfer Types (1)
Control Transfer
=>Used to configure a device (enumeration)
=>Compose of three phases (setup,data,status)
Isochronous Transfer
=>Used for multimedia devices
=>It is guarantee the required bandwidth
=>No handshake phase

## Slide 25: Transfer Types (2)
Bulk Transfer
=>Used for large burst data
=>Guarantee of delivery , no guarantee of
bandwidth or minimum latency
Interrupt Transfer
=>If there is a pending interrupt , the function
will send details to host after host poll it

## Slide 26: Packet (1)
PID：Packet Identifier Field
Address Field
=>So , there are up to 127 devices in USB

## Slide 27: Packet (2)
Token Packet
=>ADDR & ENDP define an unique endpoint

## Slide 28: Packet (3)
Data Packet

## Slide 29: Packet (4)
Handshake Packet
=>Such as ACK 、NAK 、STALL…etc.

## Slide 30: Conclusion
USB is powerful and easy to use
The complex host make the device easy to design

## Slide 31: Reference
www.google.com
www.wikipedia.com
www.studymafia.org

## Slide 32: Thanks

## Slide 33: What is USB?
Universal Serial Bus
• A computer peripheral interface
• Ubiquitous across all computer platforms
• Several variations - continues to evolve
• Hot-swapable
• Provides three advantages
  – Port expansion
  – Performance
  – Standard connection method

## Slide 34
Four wires (+5V,
Return, data twisted
pair)
• Up to 5 m (16.4 ft)
• Longer connections use
hubs or active
extensions
  – Active extension
  incorporates a buspowered
  hub